Int. No. 1176

By Council Members Dilan, Koo, Koppell, Vann, Rodriguez, Halloran and Ulrich (by request of the Mayor)

..Title

A Local Law to amend the administrative code of the city of New York and the New York city building code,  in relation to electric vehicle charging stations in open parking lots and parking garages.

..Body

Be it enacted by the Council as follows:

Section 1.  Legislative findings and intent. The Council finds that electric vehicles emit approximately 75% less carbon dioxide (CO2) than average vehicles. Pure battery electric vehicles do not emit tailpipe pollutants such as benzene and nitrogen oxide, which negatively impact city air quality and resident health. Providing for infrastructure to promote and support electric vehicle use will lead to improvement of the city’s air quality and reduce the city’s production of greenhouse gases.

Electric vehicles require chargers, or Electric Vehicle Supply Equipment (EVSEs). The vast majority of parking facilities are not currently being built to accommodate electric chargers. For many parking facilities built without EVSE-readiness, adding more than a handful of chargers will require expensive retrofits. Building parking facilities to be ready for electric vehicles incurs minimal additional costs while helping avoid expensive new wiring later. This legislation does not require installing EVSEs, but requires that the building have electrical capacity to add EVSEs to up to 20% of newly created parking stalls as needed.

§2.  Section 28-101.4.3 of the administrative code of the city of New York, as amended by a local law of the city of New York for the year 2013 amending the administrative code of the city of New York, the New York city plumbing code, the New York city building code, the New York city mechanical code and the New York city fuel gas code, relating to bringing such codes up to date with the 2009 editions of the international building, mechanical, fuel gas and plumbing codes, as proposed in Intro. 1056, is amended to add a new exception 20, to read as follows:

20. Parking garages and open parking lots.  Where an alteration of a parking garage or an open parking lot includes an increase in the size of the electric service, such alteration shall include provisions for the installation of electric vehicle charging stations in accordance with section 406.2.11 or 406.7.11 of the New York city building code, as applicable.

§3. Chapter 4  of the New York city building code is amended by adding new sections 406.2.11 and 406.7.11 to read as follows:

406.2.11 Electric vehicle charging stations. Parking garages shall be capable of supporting electrical vehicle charging stations in accordance with this section. Electrical raceway to the electrical supply panel serving the garage shall be capable of providing a minimum of 3.1 kW of electrical capacity to at least 20 percent of the parking spaces of the garage. The electrical room supplying the garage must have the physical space for an electrical supply panel sufficient to provide 3.1 kw of electrical capacity to at least 20 percent of the parking spaces of the garage.  Such raceway and all components and work appurtenant thereto shall be in accordance with the New York City Electrical Code.

Exceptions:

1. The provisions of this section shall not apply to parking garages for buildings of occupancy group M (Mercantile).

2. The commissioner may waive compliance with this section if it is determined that the parking garage is a  temporary facility that will be in service no longer than 3 years.

406.7.11 Electric vehicle charging stations. Open parking lots shall be capable of supporting electric vehicle charging stations in accordance with this section.  A minimum of 20  percent of the parking spaces in an open parking lot shall be equipped with electrical raceway capable of providing a minimum supply of 11.5kVA to an EVSE from an electrical supply panel. The raceway shall be no smaller than 1inch.  The electrical supply panel serving these parking spaces must have at least 3.1 kW of available capacity for each stall connected to it with raceway. Such raceway and all components and work appurtenant thereto shall be in accordance with the New York City Electrical Code.

Exceptions:.

1.	The provisions of this section shall not apply to parking lots for buildings of occupancy group M (Mercantile).

2.	The commissioner may waive compliance with this section if it is determined that the open parking lot is a temporary facility that will be in service no longer than 3 years.

§4. This local law shall take effect on the same date that a local law of the city of New York for the year 2013, amending the administrative code of the city of New York, the New York city plumbing code, the New York city building code, the New York city mechanical code and the New York city fuel gas code, relating to bringing such codes up to date with the 2009 editions of the international building, mechanical, fuel gas and plumbing codes, as proposed in Intro. 1056 takes effect.