Int. No. 585

By Council Members Recchia, Jr., Fidler, Gentile, Koslowitz, Rose, Williams and Ulrich

..Title

A Local Law to amend the administrative code of the city of New York, in relation to establishing limits on the emissions of volatile organic compounds.

..Body

Be it enacted by the Council as follows:

Section 1. Section 801.1 of the building code of the city of New York is amended to read as follows:

801.1 Scope. Provisions of this chapter shall govern the use of materials used as interior finishes, trim, [and] decorative materials, and adhesives and sealants.

§2. Section BC 801 of the building code of the city of New York is amended by adding a new section 801.1.3 to read as follows:

BC 801.1.3 Volatile organic compounds. These provisions shall limit the concentration of volatile organic compounds permitted in materials used as interior finishes, trim, decorative materials, adhesives and sealants.

§3.  Section 802.1 of the building code of the city of New York is amended by adding a new definition of “VOLATILE ORGANIC COMPOUND” to follow the definition of “TRIM” to read as follows:

VOLATILE ORGANIC COMPOUND. Any compound of carbon, excluding carbon monoxide, carbon dioxide, carbonic acid, metallic carbides or carbonates, and ammonium carbonate, which participates in atmospheric photochemical reactions, as specified in part 51.100 of chapter 40 of the United States code of federal regulations.

§4.  Chapter 8 of the building code of the city of New York is amended by adding a new section BC 806 to read as follows:

BC 806 VOLATILE ORGANIC COMPOUNDS

806.1 Carpet, carpet cushion and carpet adhesive. Any new carpet, carpet cushion, and carpet adhesive installed in any building shall comply with the standards in this section.

Exceptions:

1. Carpet, carpet cushion, and carpet adhesive installed in any building in occupancy group R-3 before July first, two thousand twelve.

2. Area rugs and similar non-adhered carpets.

806.1.1 Carpet cushion standards. Carpet cushion and, until July first, two thousands sixteen, carpet shall not exceed the twenty-four hour testing period concentrations of volatile organic compounds specified in Table 806.1.1.

TABLE 806.1.1

CARPET CUSHION VOLATILE ORGANIC COMPOUNDS LIMITS

| Volatile Organic Compound | Maximum Emission Factor (µg/m2 per hour) |
| --- | --- |
| Butylated hydroxytoluene | 300 |
| Formaldehyde | 50 |
| 4-Phenylcyclohexene (4PCH) | 50 |
| Total Volatile Organic Compounds | 1000 |

806.1.2 Carpet standards. Beginning July first, two thousand sixteen, carpet shall not exceed the twenty-four hour and fourteen day testing period concentrations of volatile organic compounds specified in Table 806.1.2.

TABLE 806.1.2

CARPET VOLATILE ORGANIC COMPOUNDS LIMITS

| Volatile Organic Compound | CAS# | 24-hour Testing Period | 14-day Testing Period |
| --- | --- | --- | --- |
|  |  | Maximum Emission Factor (µg/m2 per hour) | Maximum Air Concentration (µg/m2) | Maximum Emission Factor (µg/m2 per hour) |
| Acetaldehyde | 75-07-0 | 130 | 70 | 130 |
| Benzene | 71-43-2 | 55 | 30 | 55 |
| Caprolactam | 105-60-2 | 130 | 70 | 190 |
| 2-Ethylhexanoic Acid | 149-57-5 | 46 | 25 | 46 |
| Formaldehyde | 50-00-0 | 30 | 16.5 | 30 |
| 1-Methyl-2-pyrrolidinone | 872-50-4 | 300 | 160 | 300 |
| Naphthaline | 91-20-3 | 8.2 | 4.5 | 8.2 |
| Nonanal | 124-19-6 | 24 | 13 | 24 |
| Octanal | 124-13-0 | 13 | 7.2 | 13 |
| 4-Phenycyclohexene (4PCH) | 4994-16-5 | 50 | 27 | 50 |
| Styrene | 100-42-5 | 410 | 220 | 410 |
| Toluene | 108-88-3 | 280 | 150 | 280 |
| Vinyl acetate | 108-5-4 | 190 | 100 | 190 |
| Total Volatile Organic Compounds |  | 500 | 270 | NA |

806.1.3 Carpet adhesive standards. Carpet adhesive shall not exceed the twenty-four hour and fourteen day testing period concentrations of volatile organic compounds specified in Table 806.1.3.

TABLE 806.1.3

CARPET ADHESIVE VOLATILE ORGANIC COMPOUNDS LIMITS

| Volatile Organic Compound | CAS# | 24-hour Testing Period Maximum Emission Factor (µg/m2 per hour) | 14-day Testing Period Maximum Emission Factor (µg/m2 per hour) |
| --- | --- | --- | --- |
| Acetaldehyde | 75-07-0 | 130 | 130 |
| Benzothiazole | 95-16-9 | 30 | 30 |
| 2-Ethyl-1-Hexanol | 104-76-7 | 300 | 300 |
| Formaldehyde | 50-00-0 | 30 | 30 |
| Isooctylacrylate | 29590-42-9 | 690 | 690 |
| Methyl biphenyl | 28652-72-4 | 95 | 95 |
| 1-Methyl-2 Pyrrolidinone | 872-50-4 | 300 | 300 |
| Naphthalene | 91-20-3 | 8.2 | 8.2 |
| Phenol | 108-95-2 | 190 | 190 |
| 4-Phenylcyclohexene | 4994-16-5 | 50 | 50 |
| Styrene | 100-42-5 | 410 | 410 |
| Toluene | 108-88-3 | 280 | 280 |
| Vinyl acetate | 108-05-4 | 190 | 190 |
| Vinyl cyclohexene | 100-40-3 | 85 | 85 |
| Xylenes (m-, o-, p-) | N/A | 650 | 650 |
| Total Volatile Organic Compounds |  | 8000 | N/A |

806.1.4 Testing standard. Carpet, carpet cushion, and carpet adhesive covered by this section shall be tested in accordance with ASTM D5116-06 (Standard Guide for Small-Scale Environmental Chamber Determinations of Organic Emissions from Indoor Materials/Products).

806.1.5 Review. By July first, two thousand sixteen, and at least every three years thereafter, the department, in consultation with the commissioner of health and mental hygiene, shall review the standards set forth in this section and, if necessary, make recommendations for revisions to the Council.

806.2 Interior finishes, adhesives and sealants. The commissioner shall by rule establish limits on the concentration of volatile organic compounds permitted in materials used as interior finishes, trim, decorative materials, adhesives and sealants that may be used or installed in any building or structure in the city of New York. In developing such rules, the commissioner shall consult with the commissioner of health and mental hygiene. In developing such rules for interior wall, ceiling or floor finish, the commissioner shall consider the California air resources board 2007 suggested control measure. In developing such rules for adhesives and sealants, the commissioner shall consider rule 1168 of the south coast air quality management district.

806.2.1 Review. By July first, two thousand sixteen, and at least every three years thereafter, the department, in consultation with the commissioner of health and mental hygiene, shall review the rules promulgated pursuant to this section and, if necessary, shall revise such rules.

§5.  Section BC 202 of the building code of the city of New York is amended by adding a new definition for “VOLATILE ORGANIC COMPOUND” to follow the definition of “VISIBLE ALARM NOTIFICATION APPLIANCE” to read as follows:

VOLATILE ORGANIC COMPOUND. See section 802.1.

§6. Chapter 4 of title 20 of the administrative code of the city of New York is amended by adding a new subchapter 13 to read as follows:

SUBCHAPTER 13 VOLATILE ORGANIC COMPOUNDS

§20-699.7 Prohibition. It shall be unlawful to buy or sell, offer or attempt to buy or sell, or cause any person to buy or sell any materials that do not comply with section BC 806 of the building code of the city of New York.

§20-699.8 Penalties. A person violating section 20-699.7 of this subchapter shall be subject to a civil penalty of not less than two hundred fifty dollars nor more than five hundred dollars for the first violation.  Subsequent violations shall be subject to civil penalties of not less than five hundred dollars nor more than one thousand dollars for each violation.

§7. This local law shall take effect eighteen months after its enactment except that the commissioner of buildings shall take such actions as are necessary for its implementation, including the promulgation of rules, prior to such effective date.

JTB

LS# 0328-HT1-HT2

Int. 491/2006

5-20-11