Int. No. 271

By Council Members Lappin, Brewer, Gonzalez, Lander, Recchia Jr., Van Bramer, Vann, Williams, Garodnick, Arroyo, Mark-Viverito, Rodriguez and Gennaro

..Title

A Local Law to amend the New York city plumbing code and the administrative code of the city of new York, in relation to enhancing water efficiency standards.

..Body

Be it enacted by the Council as follows:

Section 1.  Section PC 202 of the New York city plumbing code is amended by adding certain definitions to be placed in appropriate alphabetical order to read as follows:

DUAL FLUSH TOILET.  A toilet that enables the user to select a high flush for solid waste or a reduced volume, low flush for liquid waste.

NON-WATER URINAL. A urinal that discharges into the sanitary drainage system but is not supplied by a water distribution system.

§2. Section 419.1 of the New York city plumbing code is amended to read as follows:

419.1 Approval. Urinals shall conform to ASME A112.19.2M, CSA B45.1 or CSA B45.5. Urinals shall conform to the water consumption requirements of Section 604.4. Urinals shall conform to the hydraulic performance requirements of ASME A112.19.6, CSA B45.1 or CSA B45.5. Non-water urinals shall conform to ANSI/ASME A112.19.19.

§3. Section 604.4 of the New York city plumbing code is amended to read as follows:

604.4 Maximum flow and water consumption. The maximum water consumption flow rates and quantities for all plumbing fixtures and fixture fittings shall be in accordance with Table 604.4.

Exceptions:

1. Blowout design toilets [3.5 gallons (13 L) per flushing cycle].

2. Vegetable sprays.

3. Clinical sinks [4.5 gallons (17 L) per flushing cycle].

4. Service sinks.

5. Emergency showers.

§4. Table 604.4 of the New York city plumbing code is amended to read as follows:

TABLE 604.4

MAXIMUM FLOW RATES AND CONSUMPTION FOR PLUMBING FIXTURES AND FIXTURE FITTINGS

| PLUMBING FIXTURE OR FIXTURE FITTING | MAXIMUM FLOW RATE OR QUANTITYb |
| --- | --- |
| Lavatory, private | [2.2]1.5 gmp at 60 psi |
| Lavatory, public (metering) | 0.25 gallon per metering cycle |
| Lavatory, public (other than metering) | 0.5 gpm at 60 psi |
| Shower heada | [2.5]2.0 gpm at 80 psi |
| Sink faucet | [2.2]1.5 gpm at 60 psi |
| Service sink | 2.5 gpm at 60 psi |
| Urinal | [1.0]0.5 gallon per flushing cycle |
| Toilet | [1.6]1.28U gallons per flushing cycle or equivalent dual flushc |

For SI: 1 gallon = 3.785 L, 1 gallon per minute = 3.785 L/m,

1 pound per square inch = 6.895 kPa.

a. A hand-held shower spray is a shower head.

b. Consumption tolerances shall be determined from referenced standards.

c. A dual flush toilet where the average of the high flush and the low flush is less than or equal to 1.28 gallons per flush.

§5. Chapter 13 of the New York city plumbing code is amended by adding a reference to ASME standard A112.19.19 to immediately follow the reference to ASME standard A112.19.14 to read as follows:

A112.19.19-2006 Vitreous China Nonwater Urinals……………………..419.1

§6. Section C102 (Waterless Urinals) of the New York city plumbing code is deleted.

§7. Subdivision 1 of section 20-689 of the administrative code of the city of New York is amended to read as follows:

(1) It shall be unlawful for any person to distribute, sell, offer for sale, buy, offer to buy, cause any person to buy or sell or import any plumbing fixture which does not [meet the standards of subdivision P.104.2 of section P.104.0 of reference standard RS-16 of the appendix to chapter one of title twenty-seven of this code] comply with the water consumption requirements of section 604.4 of the New York city plumbing code.

§8. This local law shall take effect on January 1, 2011, except that the commissioner of buildings and the commissioner of consumer affairs shall each take such measures as are necessary for its implementation, including the promulgation of rules, prior to such effective date.

JH

6-9-10 11 am

WE 1