Int. No. 575

By Council Members Garodnick, Chin, Dromm, Fidler, Foster, James, Koppell, Lander, Mark-Viverito, Mendez, Palma, Rose, Williams, Koo, Rodriguez and Lappin

..Title

A Local Law to amend the New York city building code, in relation to requiring newly constructed multi-family residences to provide adequate space to store and sort designated recyclable material.

..Body

Be it enacted by the Council as follows:

Section 1. Section BC 1213 of the New York city building code is amended by adding new sections BC 1213.4 and BC 1213.5 to read as follows:

1213.4 Central refuse storage room. Any building intended to be classified in occupancy groups R-1 or R-2 having 12 or more dwelling units shall include at least one central refuse storage room which shall provide sufficient space for the storage of both refuse and designated recyclables, source separated in accordance with the requirements of section 16-305 of the code and the rules promulgated pursuant thereto, and shall comply with the following minimum area requirements: (1) where there are to be between 12 and 23 dwelling units, the storage room shall be no less than 65 square feet in area; (2) where there are to be between 24 and 49 dwelling units, the storage room shall be no less than 100 square feet in area; (3) where there are to be between 50 and 99 dwelling units, the storage room shall be no less than 150 square feet in area; (4) where there are to be 100 or more dwelling units, the storage room shall be no less than 150 square feet in area plus one additional square foot in area for each dwelling unit over 99 units up to a maximum area of 250 square feet.

1213.5 Secondary storage rooms for refuse and recyclables. Any building intended to be classified in occupancy groups R-1 or R-2 having 12 or more dwelling units shall contain a secondary storage room for refuse and designated recyclable material on any floor with main entries to six or more dwelling units. Secondary storage rooms shall be a minimum of 10 square feet in area and shall contain separate receptacles for refuse, designated paper and cardboard, and designated metal, glass, and plastic.

Exceptions:

1. Floors with separate chutes for refuse, designated paper and cardboard, and designated metal, glass, and plastic.  Chutes for designated recyclable material shall be constructed in accordance with section 707.13 of this code.

2. Floors with a refuse access room that is constructed in accordance with section 707.13.3 of this code and such refuse access room is at least eight square feet in area.

§2.  This local law shall take effect one hundred eighty days after its enactment.

LS 668 - JJH

5-19-11