Int. No. 340

By Council Members Dilan, Brewer, Cabrera, Chin, Comrie, Fidler, Garodnick, Gonzalez, James, Koppell, Koslowitz, Lander, Mark-Viverito, Palma, Vann, Williams, Rodriguez, Van Bramer and Halloran

..Title

A Local Loaw to amend the New York city building code, in relation to increasing the allowable extension of sun control devices from building facades.

..Body

Be it enacted by the Council as follows:

Section 1. Statement of findings and purpose. Sun control devices can be used to combat heat gain in buildings, reduce glare, and improve occupant comfort. However, the New York City Building Code currently regulates sun control devices more restrictively than awnings. When placed above windows awnings are allowed to extend up to five feet into the street line, but the Building Code currently only allows sun control devices to extend ten inches from a building’s façade, decreasing their effectiveness.  The Council therefore finds that because their shading and visual impact are the same, standards for sun control devices and awnings should be equal.

§2. Section BC 202 of the New York city building code, as added by local law number 33 for the year 2007, is amended by adding the following definition to be placed in appropriate alphabetical order to read as follows:

SUN CONTROL DEVICE. An architectural projection that provides protection against solar radiation entering a building through glazed areas and is supported by the building to which it is attached. A sun control device may be installed in a fixed position,  may be retractable, rotating, or be any similar device. A fixed sun control device has no moving parts and is typically composed of horizontal overhangs or vertical fins. A retractable sun control device extends or retracts, and in the extended position casts a shadow on designated glazed portions of the building. A rotating sun control device may be of fixed or adjustable length and pivots at its base.

§3. Section BC 3101.1 of the New York city building code, as added by local law number 33 for the year 2007, is amended to read as follows:

3101.1 Scope. The provisions of this chapter shall govern special building construction including membrane structures, temporary structures, pedestrian walkways and tunnels, awnings [and], canopies, and sun control devices, marquees, signs, telecommunications towers and antennas, swimming pools and enclosures, sidewalk cafés, and fences.

§4. Section BC 3105 of the New York city building code, as added by local law number 33 for the year 2007, is amended to read as follows:

AWNINGS [AND], CANOPIES AND SUN CONTROL DEVICES

3105.1 General. Awnings [and], canopies and sun control devices shall comply with the requirements of this section, the requirements of Chapter 32 for projections over public ways, and other applicable sections of this code.

Exception: Canopies projecting over public rights-of-way governed by Title 19 of the Administrative Code and rules of the New York City Department of Transportation.

§5. Section BC 3105.3 of the New York city building code, as added by local law number 33 for the year 2007, is amended to read as follows:

3105.3 Design and construction. Awnings [and], canopies and sun control devices shall be designed and constructed to withstand wind or other lateral loads and live loads as required by Chapter 16 with due allowance for shape, open construction and similar features that relieve the pressures or loads. Structural members shall be protected to prevent deterioration. Awnings shall have frames of noncombustible material, covered with flame-resistant fabric in accordance with NFPA 701, plastic in accordance with Section 2605, sheet metal, or other equivalent material, and shall be either fixed, retractable, folding or collapsible.

§6. Section 3202.2.1.2 of the New York city building code, as added by local law number 33 for the year 2007, is amended to read as follows:

3202.2.1.2 Architectural details. Details such as cornices, eaves, bases, sills, headers, band course, opening frames, [sun control devices,] rustications, applied ornament or sculpture, grilles, windows when fully open, air conditioning units, and other similar elements may be constructed:

1. To project not more than 4 inches (102 mm) beyond the street line when less than 10 feet (3048 mm) above the ground or sidewalk level.

2. To project not more than 10 inches (254 mm) beyond the street line when more than 10 feet (3048 mm) above the ground or sidewalk level.

Exception: Architectural details that are more than 10 feet (3048 mm) above the sidewalk and that project more than 10 inches (254 mm) may be permitted subject to the approval of the Commissioner of the Department of Transportation.

§7. Section BC 3202.2.3 of the New York city building code as added by local law number 33 for the year 2007, is amended to read as follows:

3202.2.3 Awnings and sun control devices. Awnings and sun control devices constructed in accordance with Section 3105 and supported entirely from the building may project beyond the street line as follows:

3202.2.3.1 Store front awnings. Store front awnings may project beyond the street line not more than 8 feet (2438 mm), provided no part of the awning is less than 8 feet (2438 mm) above the ground or sidewalk level, except for a flexible valance which may be not less than 7 feet (2134 mm) above the ground or sidewalk level, and provided that the awning box or cover does not project more than 12 inches (305 mm).

3202.2.3.2 Awnings and sun control devices over windows or doors. Awnings and sun control devices over windows or doors may project beyond the street line not more than 5 feet (1524 mm), provided that no part of the awning or sun control device is less than 8 feet (2438 mm) above the ground or sidewalk level.

§8. This law shall take effect immediately.

LS # 953

7/14/10 11am

LR