Staff:	Baaba K. Halm

Counsel to the Committee

Laura Rogers

Legislative Attorney

Benjamin J. Goodman

Senior Legislative Policy Analyst

Ralph P. Hernandez

Legislative Financial Analyst

THE COUNCIL of

The city of New York

REPORT OF THE INFRASTRUCTURE DIVISION

ROBERT NEWMAN, LEGISLATIVE DIRECTOR

COMMITTEE ON HOUSING AND BUILDINGS

Hon. Erik Martin Dilan, Chair

April 6, 2011

PROPOSED INT. NO. 347-A:	By Council Members Garodnick, Brewer, Chin, Comrie, Fidler, Gentile, Gonzalez, James, Koppell, Lander, Mark-Viverito, Nelson, Palma, Sanders Jr., Vann, Williams, Rodriguez, Gennaro, Van Bramer and Koo

TITLE:	A Local Law to amend the administrative code of the city of New York and the New York city building code, in relation to roof coating standards.

APPLICABLE CODES:	Amends the administrative code section 28-101.4.3 and building code section BC 1504.8, section BC 1510.1 and chapter 35 of the building code.

BACKGROUND AND ANALYSIS:

On April 6, 2011, the Committee on Housing and Buildings, chaired by Council Member Erik Martin Dilan, will conduct a hearing on Proposed Int. No. 347-A, a Local Law to amend the Administrative Code of the City of New York and the New York City Building Code, in relation to roof coating standards. On October 20, 2010, the Committee heard an earlier version of this bill and received testimony from representatives of the Mayor’s Office of Long-Term Planning and Sustainability, the Department of Buildings and other persons interested in this legislation.  Amendments to the bill before the Committee today were made following this initial hearing.

By enacting Local Law 22 of 2008, New York City committed to reducing its greenhouse gas emissions by 30% by 2017 for government operations and by 30% citywide by 2030. Buildings are responsible for about 80 percent of the City’s greenhouse gas emissions.  Energy use in buildings (private and city-owned) is the largest contributing sector to the greenhouse gas emissions inventory.  In 2007, collectively, energy use in the form of electricity, natural gas, fuel oil, steam, and coal to heat, cool, power, and light City government buildings accounted for 64% of emissions.  Due to increasing greenhouse gas emissions and the city’s density, the City is experiencing a gradual increase in temperature.  According to a 2001 study by the Columbia Earth Institute for the U.S. Global Change Research Program, Climate Change and a Global City, there has been an increase of approximately 2°F in the New York region since 1900.  New York City is warmer than the surrounding suburbs (average temperatures in the largest cities can range from 5° to 10° warmer)  and this phenomenon, known as the Urban Heat Island Effect is caused by large areas of dark absorbent surfaces such as roofs, roadways and parking lots, and a lack of vegetation.

New York City has almost one billion square feet of roof area.  Conventional roof surfaces can reach temperatures of up to 185°F on a 90° day during the summer because traditional roofing materials (asphalt, bare metal or metallic) absorb and retain solar energy as heat which contributes not only to a hotter roof but also to warmer air temperatures nearby.  A roof’s absorption of solar heat sometimes leads to heat gain within the rest of the building, thereby causing discomfort for building inhabitants and increasing local cooling loads-particularly in older buildings, which tend to have less insulation.  Because warm building temperatures can lead to high energy demand during the summer months and to address environmental problems like the Urban Heat Island Effect and combined sewer overflows, in recent years there has been growing interest in “cool” (light colored) roofs.

Cool roofs refer to the use of highly reflective and emissive (“emissivity” is the tendency for a material to radiate heat that had been previously absorbed) coating materials which absorb less heat than traditional roofing materials. This coating is applied over a standard asphalt roof.  Cool roofs ideally lower rooftop temperatures and therefore lessen the heat load to a building reducing the energy needed to keep the building cool, thus, these types of roofs are viewed as an effective strategy in conserving energy and enhancing a building’s sustainability.  A cool roof coating also increases the durability of the roof membrane because it is subject to reduced thermal cycling amplitude and UV radiation. The recently revised New York City Building Code (Building Code or BC) requires that for new construction, roof coverings on low-sloped roofs or setbacks to be white in color or meet certain EnergyStar ratings.  Recently, the City announced its success in applying reflective white coating to one million square foot of rooftop as part of the NYC CoolRoofs initiative.  However, more reflective and emissive roof coating material is currently available than the coating standards required by the Building Code.  This legislation is intended to strengthen the current roof asphalt roof coating standards in order to reduce the energy needed to keep a building cool.

Proposed Int. No. 347-A

Bill section one provides the bill’s statement of findings and purpose.  In particular, this section indicates that the Council finds that the use of cool roofs as a mitigation strategy for the urban heat island effect can result in lower energy use, reduced air pollution and greenhouse gas emissions while at the same time improving health and comfort in warm weather.  Bill section one also notes that the Council further finds that studies show that North Atlantic states with relatively long heating seasons may benefit and reap net savings from cool roofs because of high electricity costs in places like New York City.  Further, on a global level, implementing the proposal will also help combat global warming and to the extent that energy demand is lessened, it can result in fewer air emissions and air quality related environmental diseases.  New York City began addressing these issues by incorporating a requirement for white roofs in the last code cycle; however there is a need to strengthen the City’s roof coating standards to require the use of more reflective and emissive materials.

Bill section two amends section 28-101.4.3 of the Administrative Code of the City of New York (Ad. Code) by adding a new item 11 to require that alteration of existing buildings (buildings subject to Building Codes in effect prior to the 2008 Building Code) involving the recovering or replacing of an existing roof covering must comply with section 1504.8 of the Building Code unless the area to be recovered or replaced is less than 50% and less than 500 square feet of the roof area.

Bill section three amends section BC 1504.8 (reflectance standards) to require roof coverings on roofs or setbacks with slope equal to or less than two units vertical in 12 units horizontal (17 percent) must have a minimum initial solar reflectance of 0.7 in accordance with ASTM C1549 or ASTM E 1918, and a minimum thermal emittance of 0.75 as determined in accordance with ASTM C1371 or ASTM E 408; or a minimum SRI (standard that incorporates both reflectance and emissivity) of 78 as determined in accordance with ASTM E 1980.  The exceptions to such asphalt coating requirements would include: terraces on setbacks comprising less than 25 percent of the area of the largest floor plate in the building; any portion of a roof covered by a green roof system, including such a system with agricultural plantings, in compliance with Section 1507.16; any portion of a roof used as outdoor recreation space by the occupants of the building that is landscaped, covered by wood decking or covered with a walking surface or other protective surface, provided that such walking surface or protective surface has a minimum initial solar reflectance of 0.3 as determined in accordance with ASTM C1549 or ASTM E1918; ballasted roofs, provided that the ballast has a minimum initial solar reflectance of 0.2 as determined in accordance with ASTM C1549 or ASTM E1918; any portion of a roof that is under mechanical equipment, flush mounted solar panels lying directly on the roof surface, duckboarding, decking, platform, roof tank, cooling tower or any other rooftop structure or equipment exempted by rule by the commissioner; any roof or portion of a roof composed of glass, metal, clay or concrete tile or plastic/rubber intended to simulate clay or concrete tile, wood, or slate; any portion of a roof used by a school or daycare center as a playground for children and any roof, if the amount of rooftop space not subject to the above identified exceptions is in the aggregate less than 100 square feet.

Bill section four amends section BC 1510.1 of the Building Code to provide that the asphalt roof covering reflectance standards identified in Section 1504.8 shall not apply if the area to be recovered or replaced is less than 50% and less than 500 square feet of the roof area.

Bill section five amends Chapter 35 of the Building Code to add certain referenced standards of ASTM International in appropriate numerical order.  The new referenced standards are identified as ASTM C1371 - 04a(2010)e1, ASTM C1549 - 09, ASTM E408 – 71(2008), ASTM E1918 - 06, and ASTM E1980 – 11.

Bill section six provides the enactment clause and states that this local law shall take effect on January 1, 2012.

Amendments to Int. 347

- Technical changes were made throughout the bill to correct inaccurate references and to provide clarity of text.

- Bill section two now amends section 28-101.4.3 of the Ad. Code to require alterations involving the recovering or replacement of an existing roof must conform to Section 1504.8 of the Building Code unless the area to be recovered or replaced is less than 50% and less than 500 square feet of the roof area.

- The bill no longer amends Section BC 1502.1 of the Building Code.

- Bill section three now provides that roof coverings on roofs or setbacks with slope equal to or less than two units (rather than three units) in 12 units horizontal (17 percent) (rather than 25 percent) must have must have a minimum initial solar reflectance of 0.7 in accordance with ASTM C1549 or ASTM E 1918, and a minimum thermal emittance of 0.75 as determined in accordance with ASTM C1371 or ASTM E 408; or a minimum SRI of 78 as determined in accordance with ASTM E 1980.  The bill previously provided that at least 75 percent of the area of roofs and setbacks, exclusive of skylights, shall have a covering with a minimum solar reflectance index in accordance with proposed Table 1504.8.

Table 1504.8

| Roof or Setback Type | Slope | Solar Reflectance Index |  |
| --- | --- | --- | --- |
| Low-sloped | <= 2:12 | 78 |  |
| Steep-sloped | > 2:12 | 29 |  |

Furthermore, the bill now includes additional exceptions to the covering requirements.  These exceptions include: any portion of a roof covered by a green roof system, including such a system with agricultural plantings; any portion of a roof that is landscaped, covered by wood decking or covered with a walking surface or other protective surface, provided that such walking surface or protective surface has a minimum initial solar reflectance of 0.3 as determined in accordance with ASTM C1549 or ASTM E1918; ballasted roofs must now have an minimum initial solar reflectance of 0.2 as determined in accordance with ASTM C1549 or ASTM E1918; any portion of a roof that is under duckboarding, decking, platform, roof tank, cooling tower; any roof or portion of a roof composed of glass, metal, clay or concrete tile or plastic/rubber intended to simulate clay or concrete tile, wood, or slate; any portion of a roof used by a school or daycare center as a playground for children and any roof, if the amount of rooftop space not subject to the above identified exceptions is in the aggregate less than 100 square feet.

- Bill section five now amends Chapter 35 of the Building Code to add certain referenced standards of ASTM International in appropriate numerical order.  The new referenced standards are identified as ASTM C1371 - 04a(2010)e1, ASTM C1549 - 09, ASTM E408 – 71(2008), ASTM E1918 - 06, and ASTM E1980 – 11.

- New bill section six provides the enactment clause and states that this local law shall take effect on January 1, 2012 rather than taking effect immediately.  This new effective date is intended to allow affected industries and property owners time to become aware of the new standards prior to enforcement by the City.

Proposed Int. No. 347-A

By Council Member Garodnick, Brewer, Chin, Comrie, Fidler, Gentile, Gonzalez, James, Koppell, Lander, Mark-Viverito, Nelson, Palma, Sanders Jr., Vann, Williams, Rodriguez, Gennaro, Van Bramer and Koo

..Title

A Local Law

To amend the administrative code of the city of New York and the New York city building code, in relation to roof coating standards.

..Body

Be it enacted by the Council as follows:

Section 1.  Legislative findings and intent. The Council finds that the use of cool roofs as a mitigation strategy for the “urban heat island effect”-- the tendency of urban areas to be hotter than their suburban surroundings because of dark absorbent surfaces and a lack of vegetation--can result in lower energy use and reduced air pollution and greenhouse gas emissions, while at the same time improving health and comfort in warm weather.  A cool roof transfers less heat to the building below so that the building stays cooler and more comfortable during the summer, resulting in the use of less energy for cooling. A cool roof coating also increases the durability of the roof membrane because it is subject to reduced thermal cycling amplitude and UV radiation. At the same time local climate and site specific factors play a role in the amount of savings achieved.  Cool roofs result in energy savings when they are most needed, during very hot summer periods subject to peak electrical demand. The disadvantages over the heating season, known as the “winter penalty”, have been found to be minimal in studies of New York City’s installations. The Council further finds that studies show that North Atlantic states with relatively long heating seasons may nonetheless benefit and reap net savings from cool roofs because of high electricity costs in places like New York City.  On a global level, implementing the proposal will also help combat global warming, because light is reflected into space rather than being turned into heat, which is then trapped in the CO2 blanket. Further, to the extent that energy demand is lessened, it can result in fewer air emissions and air quality related environmental diseases. New York City began addressing these issues by incorporating a requirement for white roofs in its last code cycle. Therefore, the Council finds that it is in the best interests of New York City to strengthen its roof coating standards to require the use of more reflective and emissive materials.

§2.  Section 28-101.4.3 of the administrative code of the city of New York is amended by adding a new item 11 to read as follows:

11. Alterations involving the recovering or replacing of an existing roof covering shall comply with section 1504.8 of the New York city building code unless the area to be recovered or replaced is less than 50 percent of the roof area and less than 500 square feet.

§3. Section BC 1504.8 of the New York city building code, as added by local law number 33 for the year 2007, is amended to read as follows:

1504.8 Reflectance.  Roof coverings on roofs or setbacks with slope equal to or less than [three] two units vertical in 12 units horizontal ([25] 17 percent) shall [be white in color or EnergyStar rated as highly reflective for at least 75 percent of the area of the roof or setback surface.] have:

- a minimum initial solar reflectance of 0.7 in accordance with ASTM C1549 or ASTM E 1918, and a minimum thermal emittance of 0.75 as determined in accordance with ASTM C1371 or ASTM E 408; or

2.  a minimum SRI of 78 as determined in accordance with ASTM E 1980.

Exceptions:

1.  Terraces on setbacks comprising less than 25 percent of the area of the largest floor plate in the building.

2. [Green roofs] Any portion of a roof covered by a green roof system, including such a system with agricultural plantings, in compliance with Section 1507.16 [shall be permitted to comprise part or all of the 75 percent required area coverage].

3. [Roofs] Any portion of a roof used as outdoor recreation space by the occupants of the building [shall be permitted to be either] that is landscaped, covered by wood decking or covered with a walking surface or other protective surface, provided that such walking surface or protective surface has [with an albedo of 30 percent or greater] a minimum initial solar reflectance of 0.3 as determined in accordance with ASTM C1549 or ASTM E1918.

4. Ballasted roofs, provided that the ballast has a minimum initial solar reflectance of 0.2 as determined in accordance with ASTM C1549 or ASTM E1918.

5. Any portion of a roof that is under mechanical equipment, flush mounted solar panels lying directly on the roof surface, duckboarding, decking, platform, roof tank, cooling tower or any other rooftop structure or equipment exempted by rule by the commissioner.

6. Any roof or portion of a roof composed of glass, metal, clay or concrete tile or plastic/rubber intended to simulate clay or concrete tile, wood, or slate.

7. Any portion of a roof used by a school or daycare center as a playground for children.

8.  Any roof, if the amount of rooftop space not subject to exceptions 1 through 7 is in the aggregate less than 100 square feet.

§4. Section BC 1510.1 of the New York city building code, as added by local law number 33 for the year 2007, is amended to read as follows:

1510.1 General. Materials and methods of application used for recovering or replacing an existing roof covering shall comply with the requirements of Chapter 15.

Exception:  Section 1504.8 shall not apply if the area to be recovered or replaced is less than 50 percent of the roof area and less than 500 square feet.

§5.  The list of referenced standards of ASTM (ASTM International) as set forth in chapter 35 of the New York city building code is amended by adding, in appropriate numerical order, new standards  ASTM C1371 - 04a(2010)e1, ASTM C1549 - 09, ASTM E408 – 71(2008), ASTM E1918 - 06, and ASTM E1980 – 11 to read as follows:

| ASTM | ASTM International 100 Barr Harbor Drive West Conshohocken, PA 19428-2959 |
| --- | --- |
| Standard reference number | Title |
| C 1371 - 04a(2010)e1 C 1549 – 09 E 408 – 71(2008) E 1918 – 06 E1980 - 11 | Standard Test Method for Determination of Emittance of Materials Near Room Temperature Using Portable Emissometers Standard Test Method for Determination of Solar Reflectance Near Ambient Temperature Using a Portable Solar Reflectometer Standard Test Methods for Total Normal Emittance of Surfaces Using Inspection-Meter Techniques Standard Test Method for Measuring Solar Reflectance of Horizontal and Low-Sloped Surfaces in the Field Standard Practice for Calculating Solar Reflectance Index of Horizontal and Low-Sloped Opaque Surfaces |  |

§6. This local law shall take effect on January 1, 2012.

3/29/2011 5:45 pm

# Footnotes

Recognizing the important role of building performance, Mayor Bloomberg and Speaker Quinn convened the New York City Green Codes Task Force in July of 2008.  The Task Force was composed of industry experts, union representatives, tenant advocates, environmentalists, academics, developers, buildings owners, and representatives of City agencies as well as the Mayor’s office and the Speaker’s office. This group was divided into nine technical committees, a steering committee, and an industry advisory committee. After two years of work examining each of New York City’s building codes, the Task Force presented 111 recommendations for “greening the codes.” The recommended improvements are intended to raise the bar for environmental performance in buildings throughout the City.

Mayor’s Office of Long-Term Planning and Sustainability, September 2009. Inventory of New York City Greenhouse Gas Emissions.

Id.

New York City Department of Design & Construction, June 2007.  DDC Cool & Green Roofing Manual.

Id.

U.S. Environmental Protection Agency Office of Atmospheric Programs.  Reducing Urban Heat Islands: Compendium of Strategies, Cool Roofs.

See note 5.

See note 6.

See Section BC 1504.8.

Mayor Bloomberg Coats One Millionth Square Foot of White Rooftop as a Part of NYC Service Cool Roofs Initiative, available at www.nyc.gov.